## Slide 1: EE-2003 Computer Organization & Assembly Language
INSTRUCTOR
Engr. Aashir Mahboob
Lecturer, Department of Computer Science
FAST NUCES (Karachi)
Aashir.mahboob@nu.edu.pk

## Slide 2
Chapter 9: Strings & Arrays

## Slide 3: Strings & Arrays
String Primitive Instructions
Selected String Procedures
Two-Dimensional Arrays
Searching and Sorting Integer Arrays

## Slide 4
String Primitive Instructions

## Slide 5: String Primitive Instructions
MOVSB, MOVSW, and MOVSD
CMPSB, CMPSW, and CMPSD
SCASB, SCASW, and SCASD
STOSB, STOSW, and STOSD
LODSB, LODSW, and LODSD

## Slide 6: MOVSB, MOVSW, & MOVSD
The MOVSB, MOVSW, and MOVSD instructions copy data from the memory location pointed to by ESI to the memory location pointed to by EDI.
Example:
  .data
  source DWORD 0FFFFFFFFh
  target DWORD ?
  .code
  mov esi, OFFSET source
  mov edi, OFFSET target
  movsd

## Slide 7: MOVSB, MOVSW, & MOVSD
ESI and EDI are automatically incremented or decremented:
  MOVSB increments/decrements by 1
  MOVSW increments/decrements by 2
  MOVSD increments/decrements by 4

## Slide 8: Direction Flag
The Direction flag controls the incrementing or decrementing of ESI and EDI.
  DF = clear (0): increment ESI and EDI
  DF = set (1): decrement ESI and EDI
The Direction flag can be explicitly changed using the CLD and STD instructions:
  CLD ; clear Direction flag
  STD ; set Direction flag

## Slide 9: Using a Repeat Prefix
By itself, a string primitive instruction processes only a single memory value or pair of values.
REP (a repeat prefix) can be inserted just before MOVSB, MOVSW, or MOVSD
ECX controls the number of repetitions
Example: Copy 20 doublewords from source to target
  .data
  source DWORD 20 DUP(?)
  target DWORD 20 DUP(?)
  .code
  cld ; direction = forward
  mov ecx,LENGTHOF source ; set REP counter
  mov esi,OFFSET source
  mov edi,OFFSET target
  rep movsd

## Slide 10: Example
Use MOVSD to delete the first element of the following doubleword array. All subsequent array values must be moved one position forward toward the beginning of the array: array DWORD 1,1,2,3,4,5,6,7,8,9,10
Solution:
  .data
  array DWORD 1,1,2,3,4,5,6,7,8,9,10
  .code
  cld
  mov ecx,(LENGTHOF array) - 1
  mov esi,OFFSET array+4
  mov edi,OFFSET array
  rep movsd

## Slide 11: CMPSB, CMPSW, & CMPSD
The CMPSB, CMPSW, and CMPSD instructions each compare a memory operand pointed to by ESI to a memory operand pointed to by EDI
  CMPSB compares bytes
  CMPSW compares words
  CMPSD compares doublewords
Repeat prefix often used
  REPE (REPZ)
  REPNE (REPNZ)

## Slide 12: Comparing a Pair of Doublewords
If source > target, the code jumps to label L1; otherwise, it jumps to label L2
Solution:
  .data
  source DWORD 1234h
  target DWORD 5678h
  .code
  mov esi, OFFSET source
  mov edi, OFFSET target
  cmpsd ; compare doublewords
  ja L1 ; jump if source > target
  jmp L2 ; jump if source <= target

## Slide 13: Comparing a Pair of Doublewords
Modify the program in the previous slide by declaring both source and target as WORD variables. Make any other necessary changes.
Solution:

## Slide 14: Comparing a Pair of Doublewords
Use a REPE (repeat while equal) prefix to compare corresponding elements of two arrays
Solution:
  .data
  COUNT = 20
  source DWORD COUNT DUP(?)
  target DWORD COUNT DUP(?)
  .code
  mov ecx, COUNT ; repetition count
  mov esi, OFFSET source
  mov edi, OFFSET target
  cld ; direction = forward
  repe cmpsd ; repeat while equal

## Slide 15: Example: Comparing Two Strings
This program compares two strings (source and destination). It displays a message indicating whether the lexical value of the source string is less than the destination string.
Solution:
  .data
  source BYTE "MARTIN "
  dest BYTE "MARTINEZ"
  str1 BYTE "Source is smaller",0dh,0ah,0
  str2 BYTE "Source is not smaller",0dh,0ah,0

## Slide 16: Example: Comparing Two Strings
  .code
  main PROC
  cld ; direction = forward
  mov esi, OFFSET source
  mov edi, OFFSET dest
  mov ecx, LENGTHOF source
  repe cmpsb
  jb source_smaller
  mov edx,OFFSET str2 ; "source is not smaller"
  jmp done
  source_smaller:
  mov edx,OFFSET str1 ; "source is smaller"
  done:
  call WriteString
  exit
  main ENDP
  END main

## Slide 17: Example: Comparing Two Strings
The following diagram shows the final values of ESI and EDI after comparing the strings:

## Slide 18: SCASB, SCASW, & SCASD
The SCASB, SCASW, and SCASD instructions compare a value in AL/AX/EAX to a byte, word, or doubleword, respectively, addressed by EDI
Useful types of searches:
  Search for a specific element in a long string or array
  Search for the first element that does not match a given value

## Slide 19: SCASB, SCASW, & SCASD
Search for the letter 'F' in a string named alpha:
Solution:

## Slide 20: STOSB, STOSW, & STOSD
The STOSB, STOSW, and STOSD instructions store the contents of AL/AX/EAX, respectively, in memory at the offset pointed to by EDI
When used with the REP prefix, these instructions are useful for filling all elements of a string or array with a single value
Example: fill an array with 0FFh

## Slide 21: LODSB, LODSW & LODSD
LODSB, LODSW, and LODSD load a byte or word from memory at ESI into AL/AX/EAX, respectively.
•The REP prefix is rarely used with LODS because each new value loaded into the accumulator overwrites its previous contents.
• Instead, LODS is used to load a single value.
Example:

## Slide 22: Array Multiplication Example
Write a program that converts each unpacked binary-coded decimal byte belonging to an array into an ASCII decimal byte and copies it to a new array.
Example:
  .data
  array DWORD 1,2,3,4,5,6,7,8,9,10
  dest BYTE (LENGTHOF array) DUP(?)
  .code
  cld ; direction = up
  mov esi,OFFSET array
  mov edi,OFFSET dest
  mov ecx,LENGTHOF array
  cld
  L1: lodsb ; load into AL
  or al,30h ; convert to ASCII
  stosb ; store into memory
  loop L1

## Slide 23: Exercixe
Write a program that converts each unpacked binary-coded decimal byte belonging to an array into an ASCII decimal byte and copies it to a new array.
  .data
  array BYTE 1,2,3,4,5,6,7,8,9
  dest BYTE (LENGTHOF array) DUP(?)
Solution:
  .code
  mov esi,OFFSET array
  mov edi,OFFSET dest
  mov ecx,LENGTHOF array
  cld ; direction = up
  L1: lodsb ; load into AL
  or al,30h ; convert to ASCII
  stosb ; store into memory
  loop L1

## Slide 24
•Although they are called string primitives, they are not limited to character arrays.
•Each instruction implicitly uses ESI, EDI, or both registers to address memory.
•String primitives execute efficiently because they automatically repeat and increment array indexes.

## Slide 25
Selected String Procedures

## Slide 26: Selected String Procedures
The following string procedures may be found in the Irvine32 and Irvine16 libraries:
  Str_compare Procedure
  Str_length Procedure
  Str_copy Procedure
  Str_trim Procedure
  Str_ucase Procedure

## Slide 27: PROTO DIRECTIVE
•Creates a procedure prototype
label PROTO paramList
•Every procedure called by the INVOKE directive must have a prototype.
•A complete procedure definition can also serve as its own prototype.
•Standard configuration: PROTO appears at top of the program listing, INVOKE appears in the code segment, and the procedure implementation occurs later in the program.

## Slide 28: EXAMPLE
• Prototype for the ArraySum procedure, showing its parameter list:

## Slide 29: Str_compare Procedure
Compares string1 to string2, setting the Carry and Zero flags accordingly
PROTOTYPE (PROTO):
  Str_compare PROTO,
  string1:PTR BYTE, ; pointer to string
  string2:PTR BYTE ; pointer to string

## Slide 30: Str_compare Procedure Source Code
  Str_compare PROC USES eax edx esi edi,
  string1:PTR BYTE, string2:PTR BYTE
  mov esi,string1
  mov edi,string2
  L1: mov al,[esi]
  mov dl,[edi]
  cmp al,0 ; end of string1?
  jne L2 ; no
  cmp dl,0 ; yes: end of string2?
  jne L2 ; no
  jmp L3 ; yes, exit with ZF = 1
  L2: inc esi ; point to next
  inc edi
  cmp al,dl ; chars equal?
  je L1 ; yes: continue loop
  L3: ret
  Str_compare ENDP

## Slide 31: Str_length Procedure
Calculates the length of a null-terminated string and returns the length in the EAX register
PROTOTYPE (PROTO):
  Str_length PROTO,
  pString:PTR BYTE ; pointer to string
Example:
  .data
  myString BYTE "abcdefg",0
  .code
  INVOKE Str_length, ADDR myString ; EAX = 7

## Slide 32: Str_length Procedure Source Code
  Str_length PROC USES edi,
  pString:PTR BYTE ; pointer to string
  mov edi, pString
  mov eax,0 ; character count
  L1:
  cmp byte ptr [edi],0 ; end of string?
  je L2 ; yes: quit
  inc edi ; no: point to next
  inc eax ; add 1 to count
  jmp L1
  L2: ret
  Str_length ENDP

## Slide 33: Str_copy Procedure
Copies a null-terminated string from a source location to a target location
PROTOTYPE (PROTO):
  Str_copy PROTO,
  source:PTR BYTE, ; pointer to string
  target:PTR BYTE ; pointer to string
Example:
  .data
  source BYTE "hello",0
  target BYTE SIZEOF source DUP (?)
  .code
  INVOKE Str_copy, ADDR source, ADDR target

## Slide 34: Str_copy Procedure Source Code
  Str_copy PROC USES eax ecx esi edi,
  source:PTR BYTE, ; source string
  target:PTR BYTE ; target string
  INVOKE Str_length,source ; EAX = length source
  mov ecx,eax ; REP count
  inc ecx ; add 1 for null byte
  mov esi,source
  mov edi,target
  cld ; direction = up
  rep movsb ; copy the string
  ret
  Str_copy ENDP

## Slide 35: Str_trim Procedure
The Str_trim procedure removes all occurrences of a selected trailing character from a null-terminated string
PROTOTYPE (PROTO):
  Str_trim PROTO,
  pString:PTR BYTE, ; points to string
  char:BYTE ; char to remove
Example:
  .data
  myString BYTE "Hello###",0
  .code
  INVOKE Str_trim, ADDR myString, '#'
  myString = "Hello"

## Slide 36: Str_trim Procedure
Str_trim checks a number of possible cases (shown here with # as the trailing character:
The string is empty
The string contains other characters followed by one or more trailing characters, as in "Hello##"
The string contains only one character, the trailing character, as in "#"
The string contains no trailing character, as in "Hello" or "H"
The string contains one or more trailing characters followed by one or more nontrailing characters, as in "#H" or "###Hello"

## Slide 37: Str_trim Procedure
Using the first definition in the table, position of EDI when SCASB stops:

## Slide 38: Str_trim Procedure Source Code
  Str_trim PROC USES eax ecx edi,
  pString:PTR BYTE, ; points to string
  char:BYTE ; char to remove
  mov edi,pString
  INVOKE Str_length,edi ; returns length in EAX
  cmp eax,0 ; zero-length string?
  je L2 ; yes: exit
  mov ecx,eax ; no: counter = string length
  dec eax
  add edi,eax ; EDI points to last char
  mov al,char ; char to trim
  std ; direction = reverse
  repe scasb ; skip past trim character
  jne L1 ; removed first character?
  dec edi ; adjust EDI: ZF=1 && ECX=0
  L1: mov BYTE PTR [edi+2],0 ; insert null byte
  L2: ret
  Str_trim ENDP

## Slide 39: Str_ucase Procedure
The Str_ucase procedure converts a string to all uppercase characters. It returns no value.
PROTOTYPE (PROTO):
  Str_ucase PROTO,
  pString:PTR BYTE ; pointer to string
Example:
  .data
  myString BYTE "Hello",0
  .code
  INVOKE Str_ucase, ADDR myString

## Slide 40: Str_ucase Procedure Source Code
  Str_ucase PROC USES eax esi,
  pString:PTR BYTE
  mov esi,pString
  L1: mov al,[esi] ; get char
  cmp al,0 ; end of string?
  je L3 ; yes: quit
  cmp al,'a’ ; below "a"?
  jb L2
  cmp al,'z’ ; above "z"?
  ja L2
  and BYTE PTR [esi],11011111b ; convert the char
  L2: inc esi ; next char
  jmp L1
  L3: ret
  Str_ucase ENDP

## Slide 41
Two-Dimensional Arrays

## Slide 42
•The two methods of arranging the rows and columns in memory: row-major order and column-major order.
•If you implement a two-dimensional array in assembly language, you can choose either ordering method.

## Slide 43: THE TWO OPERAND TYPES
Base-Index Operands
Base-Index Displacement Operands

## Slide 44: Base-Index Operand
A base-index operand adds the values of two registers (called base and index), producing an effective address
  Any two 32-bit general-purpose registers may be used (Note: esp is not used for general purpose)
[base + index]

## Slide 45: Base-Index-Displacement Operand
A base-index-displacement operand combines a displacement, a base register, an index register, and an optional scale factor to produce an effective address.
Displacement can be the name of a variable or a constant expression.
Common Format:
  [base + index + displacement]
  displacement[base + index]

## Slide 46: BASE-INDEX OPERANDS

## Slide 47: Two-Dimensional Array Example
Imagine a table with three rows and five columns. The data can be arranged in any format on the page:
  table BYTE 10h, 20h, 30h, 40h, 50h
  BYTE 60h, 70h, 80h, 90h, 0A0h
  BYTE 0B0h, 0C0h, 0D0h, 0E0h, 0F0h
  NumCols = 5
Alternative format:
  table BYTE 10h,20h,30h,40h,50h,60h,70h,80h,90h,0A0h,0B0h,0C0h,0D0h,0E0h,0F0h
  NumCols = 5

## Slide 48: Two-Dimensional Array Example
The following code loads the table element stored in row 1, column 2:

## Slide 49
Searching & Sorting Integer Arrays

## Slide 50: Searching and Sorting Integer Arrays
Bubble Sort
  A simple sorting algorithm that works well for small arrays
Binary Search
  A simple searching algorithm that works well for large arrays of values that have been placed in either ascending or descending order

## Slide 51: Bubble Sort
Each pair of adjacent values is compared, and exchanged if the values are not ordered correctly:

## Slide 52: Bubble Sort Pseudocode
N = array size, cx1 = outer loop counter, cx2 = inner loop counter:
  cx1 = N - 1
  while( cx1 > 0 )
  {
  esi = addr(array)
  cx2 = cx1
  while( cx2 > 0 )
  {
  if( array[esi] < array[esi+4] )
  exchange( array[esi], array[esi+4] )
  add esi,4
  dec cx2
  }
  dec cx1
  }

## Slide 53: Bubble Sort Implementation
  BubbleSort PROC USES eax ecx esi,
  pArray:PTR DWORD,Count:DWORD
  mov ecx,Count
  dec ecx ; decrement count by 1
  L1: push ecx ; save outer loop count
  mov esi,pArray ; point to first value
  L2: mov eax,[esi] ; get array value
  cmp [esi+4],eax ; compare a pair of values
  jge L3 ; if [esi] <= [edi], skip
  xchg eax,[esi+4] ; else exchange the pair
  mov [esi],eax
  L3: add esi,4 ; move both pointers forward
  loop L2 ; inner loop
  pop ecx ; retrieve outer loop count
  loop L1 ; else repeat outer loop
  L4: ret
  BubbleSort ENDP

## Slide 54: Binary Search
Searching algorithm, well-suited to large ordered data sets
Divide and conquer strategy
Each "guess" divides the list in half
Classified as an O(log n) algorithm:
As the number of array elements increases by a factor of n, the average search time increases by a factor of log n

## Slide 55: Binary Search

## Slide 56: Binary Search Pseudocode
  int BinSearch( int values[],
  const int searchVal, int count )
  {
  int first = 0;
  int last = count - 1;
  while( first <= last )
  {
  int mid = (last + first) / 2;
  if( values[mid] < searchVal )
  first = mid + 1;
  else if( values[mid] > searchVal )
  last = mid - 1;
  else
  return mid; // success
  }
  return -1; // not found
  }

## Slide 57: Binary Search Implementation
  BinarySearch PROC uses ebx edx esi edi,
  pArray:PTR DWORD, ; pointer to array
  Count:DWORD, ; array size
  searchVal:DWORD ; search value
  LOCAL first:DWORD, ; first position
  last:DWORD, ; last position
  mid:DWORD ; midpoint
  mov first,0 ; first = 0
  mov eax,Count ; last = (count - 1)
  dec eax
  mov last,eax
  mov edi,searchVal ; EDI = searchVal
  mov ebx,pArray ; EBX points to the array
  L1: ; while first <= last
  mov eax,first
  cmp eax,last
  jg L5 ; exit search

## Slide 58: Binary Search Implementation (Continue)
  ; mid = (last + first) / 2
  mov eax,last
  add eax,first
  shr eax,1
  mov mid,eax
  ; EDX = values[mid]
  mov esi,mid
  shl esi,2 ; scale mid value by 4
  mov edx,[ebx+esi] ; EDX = values[mid]
  ; if ( EDX < searchval(EDI) )
  ; first = mid + 1;
  cmp edx,edi
  jge L2
  mov eax,mid ; first = mid + 1
  inc eax
  mov first,eax
  jmp L4 ; continue the loop
base-index addressing

## Slide 59: Binary Search Implementation (Continue)
  ; else if( EDX > searchVal(EDI) )
  ; last = mid - 1;
  L2: cmp edx,edi ; (could be removed)
  jle L3
  mov eax,mid ; last = mid - 1
  dec eax
  mov last,eax
  jmp L4 ; continue the loop
  ; else return mid
  L3: mov eax,mid ; value found
  jmp L9 ; return (mid)
  L4: jmp L1 ; continue the loop
  L5: mov eax,-1 ; search failed
  L9: ret
  BinarySearch ENDP